## Slide 1: Design of Analog Integrated Circuit
VO Tuan minh
Faculty of Electronics and Telecommunication Engineering
University of Science and Technology - The University of Danang

## Slide 2: Chủ đề
Giới thiệu Thiết kế vi mạch & Đặc tính của MOSFET
Mạch khuếch đại đơn
Mạch khuếch đại vi sai
Mạch gương dòng & Kỹ thuật phân cực
Đáp ứng tần số
Bộ chuyển đổi tương tự/số
Bộ chuyển đổi số/tương tự
Vòng khóa pha

## Slide 3: Overview
CMOS Comparators
Analog Digital Converters

## Slide 4: Voltage comparators
A comparator detects if its input is higher or lower than a reference level.
Its output is a large voltage which is assumed to represent a digital 1 or 0 level.
If vin > vref => vout = “1”
If vin < vref => vout = “0”

## Slide 5: Design Considerations
Accuracy (offset, noise, resolution)
Settling time (tracking BW, regeneration speed)
Sensitivity (gain)
Metastability (any decision is better than no decision!)
Overdrive recovery (memory)
CMRR
Power consumption

## Slide 6: High-Gain Amplifiers
Amplify Vin (min) to VDD
=> Vin (min) determined by ADC resolution
Example: 12-bit ADC with
  Vr = 1.5V => 1 LSB = 0.36mV
  VDD = 1.8V
=> For 1.8V output & 0.5LSB precision

## Slide 7: Single-Stage Amplification
Amplifier maximum Gain-Bandwidth product (fu) for a given technology, typically a function of maximum device ft,
Example: fu = 10GHz & Av = 10,000
=> Too slow for majority of applications!
=> Cascade of lower gain stages to broaden operating frequency

## Slide 8: Open Loop Cascade of Amplifiers

## Slide 9: Offset Cancellation
In sampled-data cascade of amplifiers Vos can be cancelled
  Store on ac-coupling caps in series with amp stages
Offset associated with a specific amp can be cancelled by storing it in series with either the input or the output of that stage

## Slide 10: Output Series Cancellation
Amp modeled as ideal + Vos (input referred)
Store offset:
  S1, S4: open
  S2, S3: closed
  => VC = A⸱VOS

## Slide 11: Output Series Cancellation
Amplify:
  S2, S3: open
  S1, S4: closed
  VC = A⸱VOS
Circuit requirements:
  Amp not saturate during offset storage
  High-impedance (C) load -> Cc not discharged
  Cc >> CL to avoid attenuation
  Cc >> Csw to avoid excessive offset due to charge injection

## Slide 12: Cascaded Output Series Cancellation
Note: Offset storage in capacitors connected in series with amplifier outputs

## Slide 13: Cascaded Output Series Cancellation
S1: open
S2, S3, S4, S5: closed

## Slide 14: Cascaded Output Series Cancellation
S3: open
Feedthrough of S3: offset on X
Switch offset,  induced on X
S4 remains closed, offset
associated with  stored on C2

## Slide 15: Cascaded Output Series Cancellation
S4: open
Feedthrough of S4: offset on Y
Switch offset, 4 induced on Y
S5 remains closed, offset
associated with 4 stored on C3

## Slide 16: Cascaded Output Series Cancellation
S2, S5: open, S1: closed
Input connected to low
impedance source charge
injection: not of major concern
Switch offset,  introduced due
to S5 opening

## Slide 17: Cascaded Output Series Cancellation
Input-Referred Offset:

## Slide 18: Cascaded Output Series Cancellation
Advantages:
  Almost compete cancellation
  Closed-loop stability not required
Disadvantages:
  Gain per stage must be small
  Offset storage C in the signal path => could slow down overall performance

## Slide 19: Input Series Cancellation

## Slide 20: Input Series Cancellation
Store offset:
Note: Mandates closed-loop
stability

## Slide 21: Input Series Cancellation
Amplify:
  S2, S3: open
  S1: closed

## Slide 22: Cascaded Input Series Cancellation
2: charge injection associated with opening of S4

## Slide 23: Input Series Cancellation
Advantages:
  In applications such as C-array successive approximation ADCs can use C-array to store offset
Disadvantages:
  Cancellation not complete
  Requires closed loop stability
  Offset storage C in the signal path, could slow down overall performance

## Slide 24: Cascade of Gain Stages
Fully differential gain stages: 1st order cancellation of switch feedthrough offset
Output series offset cancellation
Input series offset cancellation
Combined input & output series
offset cancellation

## Slide 25: Latched Comparators
Compares two input voltages at time tx & generates a digital output:
  If Vi+ > Vi- => Vout = “1”
  If Vi- < Vi+ => Vout = “0”

## Slide 26: Latched Comparators
Comparator amplification need not be linear => can use a latch => regeneration
Latch => Amplification + positive feedback

## Slide 27: Simplest Form of Latch

## Slide 28: Static Latch
Active pull-up and pull-down → full CMOS logic levels
Very fast!
Q+ and Q- are not well defined in reset mode (Φ = 1)
Large short-circuit current in reset mode
Zero DC current after full regeneration
Very noisy

## Slide 29: Semi-Dynamic Latch
Diode divider disabled in reset mode → less short-circuit current
Pull-up not as fast
Q+ and Q- are still not well defined in reset mode (Φ = 1)
Zero DC current after full regeneration
Still very noisy

## Slide 30: Current-Steering Latch
Constant current → very quiet
Higher gain in tracking mode
Cannot produce full logic levels
Fast

## Slide 31: Dynamic Latch
Zero DC current in reset mode
Q+ and Q- are both reset to “0”
Full logic level after regeneration
Slow
X
Y
M
N

## Slide 32: Modified Dynamic Latch
Zero DC current in reset mode
Q+ and Q- are both reset to “0”
Full logic level after regeneration
Slow
X
Y
M
N

## Slide 33: Comparator Dynamic Behavior

## Slide 34: Comparator Resolution
Dt = (gm/C).ln(Vin1/Vin2)

## Slide 35: Latch-Only Comparator
Much faster compared to cascade of open-loop amplifiers
Main problem associated with latch-only comparator topology
  High input-referred offset voltage (as high as 100mV!)
    Solution: Use preamplifier to amplify the signal and reduce overall input-referred offset

## Slide 36: Pre-Amplifier + Latch
Latch offset attenuated by preamp gain when referred to preamp input. Assuming the two offset sources are uncorrelated
To reduce the effect of latch offset => high preamp gain desirable
Fast comparator => low preamp gain
=> Compromise speed vs. input-referred latch offset

## Slide 37: CMOS Comparator Example

## Slide 38: Overview
CMOS Comparators
Analog Digital Converters

## Slide 39: What is ADC?
An electronic circuit which transforms a signal from analog (continuous) to digital (discrete) form.
Analog signals are directly measurable quantities.
Digital signals only have two states. For digital computer, we refer to binary states, 0 and 1.
Why ADC is needed?
Microprocessors can only perform complex processing on digitized signals.
When signals are in digital form, they are less susceptible to the deleterious effects of additive noise.
ADC provides a link between the analog world of transducers and the digital world of signal processing and data handling.

## Slide 40: The Measurement & Control Loop
MUX
ANALOG
SIGNAL
PROCESSOR
A - D
CONVERTER
D - A
CONVERTER
ANALOG
SIGNAL
PROCESSOR
MUX
MICRO
PROCESSOR
OR
DSP
PROCESSOR
REFERENCE
Multiplier/Divider
Log Amplifier
rms-dc Converter
F-V/V-F Converter
Operational Amp
Differential Amp
Instrumentation Amp
Isolation Amp
N
bits
N
bits
Notes: The basic measurement and control loop measures a process variable and determines what control action needs to be performed based on the processor’s control algorithm. The measurement path takes an analog variable (such as pressure, temperature etc), signal conditions it in the analog domain before applying it to an analog-to-digital converter (ADC). The ADC provides a digital output corresponding to the value of the analog input signal relative to the reference voltage. The resolution of the converter determines the number of bits (n) in the digital representation.
On the control side, the digital word from the processor is converted to an analog value using a digital-to-analog converter (DAC). The number of digital bits which are convereted to an anlog value is determined by the resolution of the DAC.

## Slide 41: ADC process
C
Quantizing & Encoding
D
D1
D0
…
uI(t)
S
Input analog signal
uI(t)
Output digital signal
n-1
2 steps
Sampling and Holding (S/H)
Quantizing and Encoding (Q/E)

## Slide 42: Sampling and Holding
Continuous Signal
Sampling pulse
Sampled signal
Sampled and hold signal
Holding signal benefits the accuracy of the A/D conversion
Minimum sampling rate should be at least twice the highest data frequency of the analog signal

## Slide 43: Quantizing and Encoding
Resolution: The smallest change in analog signal that will result in a change in the digital output.
Vr : Reference voltage
N: Digital number of bits (Resolution of the ADC)
LSB: Resolution

## Slide 44: Quantizing and Encoding
Quantizing:
Partitioning the reference signal range into a number of discrete quanta, then matching the input signal to the correct quantum.
Encoding:
Assigning a unique digital code to each quantum, then allocating the digital code to the input signal.
Analog Signal
Digital Output in Binary

## Slide 45: IDEAL ADC input vs. output
DIGITAL OUTPUT
1 LSB
ANALOG INPUT
1/8 2/8 3/8 4/8 5/8 6/8 7/8
001
010
011
100
101
110
111
Ideal ADC code transitions are exactly 1 LSB apart.
For an N-bit ADC, there are 2N codes.
Each “step” is centered on an eighth of full scale
Notes: This shows the conversion relationship for an ideal 3-bit converter. The smallest resolvable signal is 1 LSB which is equal to FS/23 or FS/8. The digital output has 8 discrete values representing a linear transfer function.

## Slide 46: Quantization Noise
001
010
011
100
101
110
111
1/8
2/8
3/8
4/8
5/8
6/8
7/8
FS
NORMALIZED ANALOG INPUT
DIGITAL OUTPUT
quantization noise error
q = 1 LSB
Notes: We have previously talked about quantization errors and how they determine dynamic range etc. This plots shows the profile of the quantization error as it tracks a ramped analog input voltage. At the centre of each of the codes, the quantization error is 0. As the input voltage increases but the digital code remains constant, the quantization error goes negative. At the next code transition, the digital output now jumps ahead of the analog input voltage ramp and quantization error jumps positive. The profile is repeated at each code of the ADC transfer function.

## Slide 47: Quantization Noise (con’t)
0 volts
+q/2
-q/2
The RMS value of the quantization noise sawtooth is its peak value, q¸2, divided by Ö3, or q¸Ö12
For Sine Wave Full Scale RMS Value is 2(N-1)q/Ö2
Thus S/N (in amplitude) is 1.225 x 2N
Expressed in dB [20log10(S/N)] as 1.76 + 6.02N
Notes: Read through Bullets

## Slide 48: Quantization Noise (con’t)
OUTPUT
FSIGNAL
FS/2
FS
RMS
QUANTIZATION NOISE
HARMONICS OF FSIGNAL
(EXAGGERATED FOR CLARITY)
If the quantization noise is uncorrelated with the frequency of the AC input signal, the noise will be spread evenly over the Nyquist bandwidth of Fs/2.
If, however the input signal is locked to a sub-multiple of the sampling frequency, the quantization noise will no longer appear uniform, but as harmonics of the fundamental frequency
Notes: A graphical representation of this RMS error in the frequency domain is shown and is called quantization noise, also referred to as noise spectral density. Remember, this is the quantization error in an ideal converter and is uniformly distributed across frequencies. One thing to note is this is sometimes also called the noise floor. And that the magnitude is dependent on the quantization level (resolution) and sample rate. It’s easy to see that with the same resolution converter, by doubling the sampling rate, the noise floor gets spread over a wider bandwidth. This is called processing gain. By doubling the sample rate, one obtains a 3dB improvement (lowering) of the noise floor or sometimes called “3dB of processing gain”.

## Slide 49: Accuracy of A/D Conversion
There are two ways to best improve the accuracy of A/D conversion:
  increasing the resolution which improves the accuracy in measuring the amplitude of the analog signal.
  increasing the sampling rate which increases the maximum frequency that can be measured.

## Slide 50: Accuracy of A/D Conversion
Time
Resolution
Time
Resolution
Low Accuracy  Improved

## Slide 51: Types of ADC
Dual Slope
Successive Approximation Register
Flash
Delta-Sigma
Pipelined Sub-ranging

## Slide 52: Dual Slope A/D Converter
Fundamental components
  Integrator
  Electronically Controlled Switches
  Counter
  Clock
  Control Logic
  Comparator

## Slide 53: How does it work?
A dual-slope ADC integrates an unknown input voltage (VIN) for a fixed amount of time (TINT), then "de-integrates" (TDE-INT) using a known reference voltage (VREF) for a variable amount of time.
The key advantage of this architecture over the single-slope is that the final conversion result is insensitive to errors in the component values. That is, any error introduced by a component value during the integrate cycle will be cancelled out during the de-integrate phase.

## Slide 54: How Does it Work Cont.?
At t < 0, S1 is set to ground, S2 is closed, and counter = 0.
At t = 0, a conversion begins and S2 is open, and S1 is set so the input to the integrator is Vin.
S1 is held for TINT which is a constant predetermined time interval.
When S1 is set the counter begins to count clock pulses, the counter resets to zero after TINT
Vo of integrator at t = TINT is VINTINT/RC is linearly proportional to VIN
At t = TINT, S1 is set so -Vref is the input to the integrator which has the voltage VINTINT/RC stored in it.
The integrator voltage then drops linearly with a slope of -Vref/RC.
A comparator is used to determine when the output voltage of the integrator crosses zero
When it is zero the digitized output value is the state of the counter.

## Slide 55: Dual Slope A/D Converter
PROS
Conversion result is insensitive to errors in the component values.
Fewer adverse affects from “noise”
High Accuracy
CONS
Slow
Accuracy is dependent on the use of precision external components
Cost

## Slide 56: Successive Approximation ADC Circuit
Uses a N-bit DAC to compare DAC and original analog results.
Uses Successive Approximation Register (SAR) supplies an approximate digital code to DAC of VIN.
Comparison changes digital output to bring it closer to the input value.
Uses Closed-Loop Feedback Conversion

## Slide 57: Successive Approximation
Capable of high speed and reliable
Medium accuracy compared to other ADC types
Good trade-off between speed and cost
Capable of outputting the binary number in serial (one bit at a time) format.
Disadvantages
Higher resolution successive approximation ADC’s will be slower
Large are due to capacitors
Advantages

## Slide 58: Flash A/D Converter
Fundamental Components (For N bit Flash A/D)
  2N-1 Comparators
  2N Resistors
  Control Logic

## Slide 59: How does it work?
Uses the 2N resistors to form a ladder voltage divider, which divides the reference voltage into 2N equal intervals.
Uses the 2N-1 comparators to determine in which of these 2N voltage intervals the input voltage Vin lies.
The Combinational logic then translates the information provided by the output of the comparators
This ADC does not require a clock, so the conversion time is essentially set by the settling time of the comparators and the propagation time of the combinational logic.

## Slide 60: Flash A/D Converter
PROS
Very Fast (Fastest)
Very simple operational theory
Speed is only limited by gate and comparator propagation delay
CONS
Expensive
Prone to produce glitches in the output
Each additional bit of resolution requires twice the comparators.

## Slide 61: SIGMA-DELTA A/D Converter
Main Components
  Resistors
  Capacitor
  Comparators
  Control Logic
  DAC

## Slide 62: How does it work?
Input is over sampled and goes to integrator.
The integration is then compared to ground.
Iterates and produces a serial bit stream
Output is a serial bit stream with # of 1’s proportional to Vin
With this arrangement the sigma-delta modulator automatically adjusts its output to ensure that the average error at the quantizer output is zero.
The integrator value is the sum of all past values of the error, so whenever there is a non-zero error value the integrator value just keeps building until the error is once again forced to zero.

## Slide 63: Sigma-Delta A/D Converter
PROS
High Resolution
No need for precision components
CONS
Slow due to over sampling
Only good for low bandwidth

## Slide 64: ADC Types Comparison
0
5
20
25
ADC Resolution Comparison
Dual Slope
Flash Successive Approx
Sigma-Delta
10 15
Resolution (Bits)
Type | Speed (relative) | Cost (relative)
Dual Slope | Slow | Med
Flash | Very Fast | High
Successive Appox | Medium – Fast | Low
Sigma-Delta | Slow | Low

## Slide 65: Pipelined Sub-ranging ADC
Conversion divided into discrete stages thus causing pipeline delay
  1st Stage ADC is 6-bit FLASH
  2nd Stage ADC is 7-bit Flash
  Total resolution is 12 bits (one bit used for error correction)
Notes: The subranging architecture is a great way to achieve higher resolutions. For example a 12-bit flash ADC would need (212-1 = 4095) comparators, but a sub-ranging ADC only needs (26-1 + 27-1 = 190) comparators. The additional circuitry needed is much less than the fewer comparators needed. The reduction in circuitry is what provides the lower power and die size.
The operation of a sub-ranging ADC is much like the successive approximation ADC except it resolves more than one bit at a time. For this example, the ADC does a rough 6-bit conversion, (result is code X). The result of this conversion is passed to a DAC which outputs a “perfect” analog reference for code X. The difference between the actual analog input and the “perfect” output of the DAC is passed to second ADC which makes fine conversion.
The output of the two conversions is combined using logic into one 12-bit word. Note, an extra bit of resolution is needed in the second ADC in order to perform error correction. Error correction is needed because of offsets between the two stages.

## Slide 66: Pipelined Sub-ranging ADC
Notes: This slide shows an example of how a sub-ranging ADC works. First, the rough ADC does a conversion. The DAC creates a reference voltage which is compared to the original analog signal. The resulting residue signal is then gained up and passed to a second “fine” ADC. The entire range of the second converter should equate to one “step” of the first ADC. After the second ADC is finished the complete word is put together. For this example, the output would be 101001. Note: no error correction is show in this example.

## Slide 67: Pipelined Sub-ranging ADC
Advantages to Pipelined Sub-ranging A/D converters
  Higher resolutions at high-speeds
  Digitize wideband inputs
Tradeoffs to pipelined sub-ranging A/D converters
  Higher power dissipation
  Larger die size
Typical Applications
  Communications
  Medical imaging
  Radar
Notes: This slide shows an example of how a sub-ranging ADC works. First, the rough ADC does a conversion. The DAC creates a reference voltage which is compared to the original analog signal. The resulting residue signal is then gained up and passed to a second “fine” ADC. The entire range of the second converter should equate to one “step” of the first ADC. After the second ADC is finished the complete word is put together. For this example, the output would be 101001. Note: no error correction is show in this example.

## Slide 68: Analog Input Signal Definitions
Notes: There are various different types of analog inputs and this slide explains the differences between them.
The first diagram shows a Unipolar, Single Ended analog input signal. The analog input is applied to the VIN pin of the ADC, has an amplitude of the Full scale input voltage (FS) and spans from 0V to +FS. The second diagram shows a Unipolar, Fully Differential analog input signal. In this case, the ADC has a positive and a negative analog input, VIN+ and VIN-. These inputs are driven by two equal signals which span from 0 V to +FS, that are 180° out of phase.
The third diagram shows a Bipolar, Single Ended analog input signal. The analog input is applied to the VIN pin of the ADC, has an amplitude of ±FS/2 and is centered on ground. The fourth diagram shows a Bipolar, Fully Differential analog input signal. In this case, the ADC has a positive and a negative analog input, VIN+ and VIN-. These inputs are driven by two equal signals of amplitude ±FS/2, that are 180° out of phase. The two inputs are centered on ground. The fifth diagram shows a Pseudo Differential analog input signal. In this case, the ADC has a positive and a negative analog input, VIN+ and VIN-. The positive input is driven by a signal of amplitude FS, and the negative input is driven by a small DC voltage to provide an offset from ground or a ‘pseudo ground’ for the VIN+ signal.

## Slide 69: Unipolar and Bipolar Converter Codes
0
0
0
FS - 1LSB
FS - 1LSB
FS - 1LSB
ALL
"1"s
1 AND ALL "0"S
ALL
"1"s
UNIPOLAR
OFFSET BINARY
2’s COMPLEMENT
-FS
-(FS - 1LSB)
Notes: This slide shows the ideal transfer function of three A/D converters with different digital code representations of an analog input signal. The unipolar transfer function (left-most plot) represents an A/D converter which handles an analog input range from 0 to +FS (Full Scale). The digital output code goes from all 0’s for an analog input voltage of 0V to all 1’s for an analog input voltage of FS–1 LSB. This code format is oftentimes called straight (or natural) binary. The number of discrete values along the way depends on the resolution of the converter.
The middle plot shows the transfer function for an A/D converter which handles a bipolar input range from –FS to +FS. In this case, the digital code is called offset binary where a digital output code of all 0’s represents –FS, a code of 1 and all 0’s (I.e. MSB is 1 and all other bits are 0) represents an analog input of 0V and a code of all 1’s represents an anlog input of FS-1LSB.
Finally, the 3rd plot represents an A/D converter which handles the same analog input voltage range as that just described but represents the digital output via 2’s complement coding. This coding is the same as that just outlined for the offset binary case but has the MSB of the digital word inverted. In effect, this MSB acts like a sign bit which is one for negative signals.

## Slide 70: Offset And Gain for Unipolar Ranges
ACTUAL
OFFSET
ERROR
WITH GAIN ERROR:
OFFSET ERROR = 0
ACTUAL
IDEAL
IDEAL
ZERO ERROR
NO GAIN ERROR:
ZERO ERROR = OFFSET ERROR
0
0
GAIN
Notes: Up to now, the transfer functions shown have been for ideal A/D converters. However, this is not the case in the real world and there are error sources in the A/D converter which will result in a non-ideal transfer function. Let’s look first at two sources of linear error, offset and gain.
First, we will look at the effects of these errors on the transfer function of a unipolar A/D converter. The effect of the offset error is to shift the entire transfer function either up or down (the example shown is for moving the transfer function up, representing a positive offset error). The offset error shifts every code of the A/D converter by an equal amount. Therefore, if the A/D converter has an offset of +2LSB, each digital output code will be shifted by +2LSB from its ideal representation.
The effect of gain error is shown in the right-hand plot. The transfer function shown assumes no offset error. The gain error has the effect of changing the slope of the transfer function. From an absolute value perspective, the gain error shifts each digital output code by a different amount. However, the effect is linear with each output being changed by an equal percentage of its correct value.

## Slide 71: Offset And Gain for Bipolar Ranges
ACTUAL
OFFSET
ERROR
WITH GAIN ERROR:
OFFSET ERROR = 0
ZERO ERROR RESULTS
FROM GAIN ERROR
ACTUAL
IDEAL
IDEAL
ZERO ERROR
ZERO ERROR
NO GAIN ERROR:
ZERO ERROR = OFFSET ERROR
0
0
Notes: This shows the effects of offset and gain errors on A/D converters with bipolar transfer functions. Of note here is the distinction between offset error and zero error. In this case, the true offset error is seen at negative full scale. However, for many bipolar A/D converters, the user is interested in the deviation from ideal at 0V analog input (zero error). With no gain error, the offset error and zero error are the same. However, when gain error effect is shown (as in the right-hand plot), there is a zero error in the A/D transfer function whereas there is no offset error.

## Slide 72: DC Specifications (DNL)
Differential Non-Linearity (DNL) is the deviation of an actual code width from the ideal 1 LSB code width
Results in narrow or wider code widths than ideal and can result in missing codes
Results in additive noise/spurs beyond the effects of quantization
Notes: The ideal width for each code is 1LSB but in practice each code width is different from its neighbours. A DNL error is defined as the difference between the ideal 1 LSB step and the actual (real) step as one moves along the transfer function (DNL = actual - ideal). Thus, in the plot shown above, we are measuring the actual width of each code. For example a code with a width of 1.5 lsb would have a DNL of 1.5 - 1.0 = 0.5 lsb. A missing code would have a width of zero and would have a DNL of 0 - 1.0 = -1.0 lsb. DNL can never be less than -1.0, but has no upper limit.
The effect of DNL error is to add “noise/spurs” to an ideal transfer function. This reduces the accuracy of the conversion beyond the limitations of quantization.

## Slide 73: Missing Codes
Many A/D converter data sheets specify “no missing codes” as this specification can be critical in some applications, such as in servo systems.

## Slide 74: DC Specifications (INL)
Integral Non-Linearity (INL) is the deviation of an actual code transition point from its ideal position on a straight line drawn between the end points of the transfer function.
INL is calculated after offset and gain errors are removed
Results in additive harmonics and spurs
Notes: INL error is not a measure of code width. It is a measure of the error in a code’s transition point. Ideally, the transition points should occur at exactly the 1/8th, 1/4th, etc voltages. Errors in the converter cause the actual code transitions to deviate from ideal. INL is usually measured with respect to code centres and is the worst deviation of any code centre from an ideal straight line drawn between the endpoints of the transfer function. This ideal straight line is calculated after both offset and gain errors are removed. Thus, in the plot shown above, we are measuring the deviation of its actual transition point from its ‘ideal’ transistion point after gain and offset are removed.
Just like DNL, INL results in a reduction in accuracy of the converter. However, unlike DNL, INL errors can result in added harmonic components. (This will be demonstrated on the next slide.)

## Slide 75: Nyquist Bandwidth & Aliasing
2 signals that are mixed together produce sum and difference frequency components
Nyquist theory stipulates that the signal frequency, FSIGNAL must be < to ½ FSAMPLING to prevent a condition known as “aliasing”, in which the difference component appears within the signal bandwidth of interest
Notes: Read Through Bullets

## Slide 76: The Nyquist Bandwidth & Aliasing
1 MHz
4 MHz
fsampling
fsampling + fsignal
fsampling - fsignal
signal
passband
3 MHz
5 MHz
fsignal
The signal frequency is < 1/2 the sampling frequency and so the sum and difference components fall outside (beyond) the signal passband
Notes: The Signal Frequency Is < 1/2 the Sampling Frequency and so the Sum and Difference Components Fall Outside (Beyond) the Signal Passband

## Slide 77: The Nyquist Bandwidth & Aliasing
The signal frequency is > 1/2 (approx 2/3) the sampling frequency. An “alias” or false image is thus created that falls within the passband of interest.
fsampling- fsignal
fsignal
fsampling
fsampling + fsignal
2.5 MHz
1.5 MHz
1 MHz
“Alias”
0.5 MHz
Notes: The Signal Frequency Is > 1/2 (approx 2/3) the Sampling Frequency. An “Alias” or False Image is Thus Created that Falls Within the Passband of Interest. There are specific applications where the input signal is bandlimited whereby the A/D converter can actually resolve input frequencies which are beyond the Nyquist frequency. These applications are known as undersampling applications.

## Slide 78: Aliasing in time domain

## Slide 79: SINAD, ENOB and SNR
SINAD (Signal-to-Noise-and-Distortion Ratio)
  The ratio of the rms signal amplitude to the mean value of the root-sum-squares (RSS) of all other spectral components, including harmonics, but excluding dc
ENOB (Effective Number of Bits)
SNR (Signal-to-Noise Ratio, or Signal-to-Noise Ratio Without Harmonics)
  The ratio of the rms signal amplitude to the mean value of the root-sum-squares (RSS) of all other spectral components, excluding the first five harmonics and dc
Notes: One of the basic ADC figures of merit is its ability to convert the signal of interest and keep it separate from other noise elements within the signal chain. It’s best defined as the ratio of the rms signal amplitude to the mean value of the root sum squares of all the spectral components. SINAD is this ratio that includes all harmonics. SNR is this ratio but it excludes the first 5 harmonics. ENOB or effective number of bits is another figure of merit and can be derived from SINAD.
It is interesting to note that SNR does depend on signal input level. In an ideal converter, the higher the input level, the higher the SNR. Unfortunately, in the real world the ADC has a maximum input level. Take this plus the fact that it is not an ideal converter, there is a slightly different curve. (solid line vs the dotted line)
======================================
Clipping …in the ADC defines the SNRmax (full scale range)
Delta between are based on the errors introduced in the Rx signal chain…. A perfect converter, quant error exists… other errors intro’d into signal chain (and others within the ADC)… increase this delta.

## Slide 80: SFDR and THD
SFDR = The difference between the rms power of the fundamental and the largest spurious signal in a given bandwidth
THD = The ratio of the rms sum of the first six harmonics to the amplitude of the fundamental
Notes: Spurious free dynamic range and total harmonic distortion are easily explained by this picture. SFDR is the distance between the signal of interest and the highest spur, including harmonics. THD is the distance relative to the signal of interest and the rms sum of a defined set of harmonics. SNR is the distance (ratio) from the signal of interest to the noise floor.

## Slide 81: ADC Figures of Merit
Sometimes inverse of this metric is used
In typical circuits power ~ speed, FOM captures this tradeoff correctly
How about power vs. ENOB?
  One more bit 2x in power?